## Slide 1: The soldering iron
Nathan Bruggeman

## Slide 2: A quick preview
Introduction; What did I build? What does it do? What are the main characteristics of the device?
Material and methods; Which components? Quick walkthrough of the construction process.
Results; How does every aspect of my device work?
Discussion; Where there any issues? How to solve them?
Notes: First there is a word about this build, what is does and what the main characteristics are. There is also an explanation of some of the most important components and is a quick walkthrough of the construction process to make it. Each electric part of the soldering iron will be discussed and the working of every aspect of the electrical circuit will be explained. There is also a discission with the problems and how to fix them.

## Slide 3: Introduction
Soldering iron
Type; temperature regulation
450 degrees
Notes: Here you can see a photo of the soldering iron. Important to know is the type of the device. It is a temperature regulation soldering iron. These are the most common type of soldering irons. The iron can be set on the desired temperature by an encoder. This soldering iron has a temperature range from 0 degrees to 450 degrees.

## Slide 4: Materials and methods
0805 SMD resistors and capacitors
THT capacitors, coils, diodes, transistors, IC’s, power relay, etc.
Atmega4809-PF
Toriodal transformer
42R series IEC connector
4-digit 7-segment display
Rotary encoder
Oem Jbc C245 soldering pen
Notes: Are 0805 SMD resistors and capacitors used. There are also THT capacitors, coils, diodes, transistors, IC’s, power relay and not to forget the ATmega4809-PF. This microcontroller for sending right information components. brain of whole device. works with a 42R series EIC connector protected with a 250V by 0.63A fuse. There is a 4-digit 7-segment display controlled by a TM1637 controller. Will use the Oem Jbc C245. Temperature of this pen is configured with the rotary encoder.

## Slide 5: Materials and methods
Mouser, Conrad, TME
Altium Designer
JLCPCB
Autodesk Fusion 360
Prusa Mini (slicer)
Soldering and testing
Notes: Most of the components are ordered on mouser. The components that are not available on Mouser are bought on Conrad and TME. The toroidal transformer comes from TME. The electric design and the PCB are designed on Altium Designer. The PCB is ordered on JLCPCB. The case is modeled on Autodesk Fusion 360. The case is sliced with the Prusa slicer app on a laptop and it is printed on the school’s Prusa Mini 3D printer. When the PCB arrives, it is time to solder all the components.

## Slide 6: Results
Power supply
Regulator
Amplifier
CPU
Notes: Fed by one toroidal transformer. One secondary winding is used for the +5V power supply for the logic and control circuits trough the bridge rectifiers and IC1. There is a Zener diode that is used as overvoltage protection. The regulator; the temperature of the pin on the soldering iron is PWM-sent by the power controlled by the transistors. They are used to regulate electric current. Around IC2A and IC2B are 2 opamp circuits that amplify the voltage on the temperature sensor terminal. The CPU is the AT which is a 8-bit microcontroller that controls the components.

## Slide 7: Discussion
Components out of stock
Postage costs
Wrong footprints
3D printing
Notes: There are a few problems with finding all the right components but as said before there are found on Conrad and TME. The postage costs on Mouser are pretty high so order together.
When trying to solder the components watch out for footprints that are not right on mouser. If there are still some, this is fixed by soldering cables onto the PCB and connecting these cables to the right pins of the component.